## Slide 1: Network Performance Analysis and Management for Cyber-Physical Systems and their Applications
William Emfinger
Vanderbilt University/ISIS
The DARPA System F6, AFRL RESOS, and AFRL SURE Projects supported this work. Any opinions, ﬁndings, and conclusions or recommendations expressed in this material are those of the authors and do not reﬂect the views of DARPA or AFRL.

## Slide 2: Outline
Introduction
Related Work
Results:
  Design-Time Network Performance Analysis of Distributed CPS Applications
    Precise Network Performance Prediction
    Comparison with Network Calculus
    Analysis of Periodic Systems
    Analysis of TDMA Scheduling
    Compositional Analysis
    Delay Analysis
    Analysis of Statically Routed Networks
  Run-Time Network Performance Monitoring and Management for Distributed CPS Applications
    Measurement, Detection, and Enforcement
    DDoS Detection
Conclusions and Future Work
Publications

## Slide 3: Introduction
Cyber-Physical Systems (CPS):
  According to NIST: CPS are smart systems that include co-engineered interacting networks of physical and computational components
  Embedded computers, sensing/actuation software, tightly coupled physical system
  Communications network (wireless) acts as backbone for cooperation between nodes
  Network resources provided as a service to users
Network resource availability affected by both application load and system’s environment
  Bandwidth (bits/sec)
  Buffering delay and transmission delay
  Availability of network resources
  Some systems may have deterministic, time-varying network characteristics or application network load (or both)
Design-time analysis is critical for applications which require tight and/or real-time guarantees
  Use the analysis to perform test for admission into the system
Image Credit: DARPA
Notes: Capacity; what exactly is bw/latency, bit/s over averaging interval
Define what we mean by applications : mention that we’re looking at application platforms, want to run wide variety of applications on the platform, need to make sure they will work on the platform
Make sure to keep distinction between network/system/application
Mention IoT thingies; focus on satellites because of challenging features
Mention why this is a special class inside of CPS:
managed remotely,
costly to operate,
need assurances (difficult to replace/repair)
Not a general purpose system/application

## Slide 4: Related Work
Current research and techniques for predicting system performance and managing resources

## Slide 5: Network Analysis through Simulation / Emulation
Discrete Event-based Simulation
  Relevant events stepped through sequentially
  Model state changes only at simulated time steps
  Scaling Issues
OMNET++ [A. Varga, 2008]
  Simulates network traffic passing through the network layers
NS-2 [D. Mahrenholz, 2004]
  Single-threaded
  Allows both simulation and emulation
  Accuracy issues [G. Lucio, 2003]
Emulation
  Use real system or testbed
  Shape network traffic to enforce proper bandwidth/delay based on models of network
Dummynet [L. Rizzo, 1997, 2010]
  Uses Linux’s underlying network traffic shaping and policing tools
  Runs on system nodes or specific network emulation nodes
OpenFlow [O. S. Consortium, 2009]
  Runs on compatible network hardware (e.g. a smart switch)
  Acts on traffic as it flows through the switch
Simulation and Emulation are both widely used for system analysis and performance prediction, but may not capture relevant behavior
Cannot provide the types of performance guarantees described in the previous section
Notes: Mention specific accuracy issue (mention why the built emulab)
Don’t model channel interference : need to state this
Mention emulab when talking about emulation
Wireless emulation possibly difficult, not possible with many widely-used tools
Some labs do
Open Systems Interconnection Model (OSI):
Physical (DSL, USB)
  Electrical and physical specs
Data Link (PPP, IEEE 802.2)
  Node to Node
  MAC
  Physical error detection
Network (IPv4/6)
  Routing
  fragmentation
Transport (TCP,UDP)
  reliability
Session (RPC)
Presentation (ASCII, JPEG)
Application (HTTP,FTP)
-----
Capturing system behavior from simulation/emulation is difficult: worst-case or edge-case behavior may not be represented

## Slide 6: Queuing Theory
Probabilistic approach to analysis of processing/communications networks [Giambene, 2005][Kendall, 1953]
Queuing system described by
  : Type of the arrival process
  : Request service time characteristics
  : Number of servers
  : Queue length
  : Number of Producers
Probabilistic analysis techniques provide probabilistic guarantees about performance and resource utilization
  Useful for analysis of system steady state
  Critical systems require deterministic performance analysis to determine stability of the system
Notes: Weak for non-steady state
Stick to probabilistic; not stochastic

## Slide 7: Deterministic Network Analysis : Network Calculus [Le Boudec, 2001][Cruz, 1991]
Based on (min,+)-calculus
Abstracts network traffic and computing nodes as arrival curves and traffic shaping service curves
Analytically predicts worst-case buffer requirements and application buffering delay
Applies system-theory concepts to computer network analysis
  Input function (data input flow) convolved with a system function (shaper) to produce the output function (data output flow)
Allows the calculation of deterministic performance bounds on
  Buffering delay
  Buffer backlog
Notes: Say exactly what (min,+)-calculus is
Make sure to mention it’s not the same convolution
Mention exactly the backlog and why it exists (simple explanation is better)

## Slide 8: Real-Time Calculus
Builds from Network Calculus, Max-Plus Linear System Theory and Real-Time Scheduling [Thiele, 2000]
Designed to analyze systems which provide computation or communication services
  Request curves vs. Capacity curves
Specifies upper/lower arrival curves () and upper/lower service curves (), which are functions of time-window size
Computes request curve for a (possibly periodic) task model specified as a directed acyclic graph (DAG), G(T) to determine schedulability
  Similarly to Network Calculus, RTC enables derivation of the computation backlog bounds
Notes: Talk about the fig in the top, explain capacity and demand as it flows through the network
GPS: generalized processor sharing
EDF : earliest deadline first
FP : fixed priority
BS: best effort?
The graph’s vertices represent subtasks and each have their own associated
Required computation time e(u)
relative deadline d(u) specifying that the task must be completed d(u) units of time after its triggering
Two vertices in G(T) may be connected by a directed edge (u;v)
which has an associated parameter p(u;v) specifies the minimum time that must elapse after the triggering of u before v can be triggered
P(T) is the period of task T
Most researchers are still using QT, but many want more precise descriptions of application traffic and performance

## Slide 9: Results
New techniques for increasing the precision of system analysis and resource management

## Slide 10: Network Performance Analysis for CPS Applications
To address the issues described above, we have developed a network modeling paradigm similar to Network Calculus’ arrival curves and service curves, called Precise Network Performance Prediction (PNP2)
In contrast to Network Calculus, we precisely model the network traffic as a function of time, i.e. bits produced or serviced as functions of time
Convolve the application data profile with the network capacity profile to obtain transmitted data profile
  r[t] : application (required) data profile
  p[t] : network (provided) capacity profile
  o[t] : the transmitted (output) data profile
Assumptions:
  Know at design-time how the application and the network will perform
  Time-Synchronization between the nodes
  State-less transmission protocols, e.g. UDP
  No packet loss or transmission errors

## Slide 11: Network Performance Analysis for CPS Applications
Notes: Spend time on the figure; really explain it

## Slide 12: PNP2 Accuracy and Comparison with NC
Validated the accuracy of PNP2 predictions using custom network traffic generation code and a network testbed
  Used Dummynet to perform traffic shaping and link emulation
Integrated Network Calculus model into PNP2 tool, allows analysis of PNP2 model using NC’s semantics
  Enables direct, easy comparison between analysis techniques
Network Calculus defines arrival curves and service curves as functions of time-window size, therefore it cannot precisely analyze systems where the applications’ data production is tightly coupled with the service capacity of the system
  i.e. applications know a prioi when the system will have high network capacity and are designed to send their data at that time

## Slide 13
PNP2
 | Network Calculus | PNP2 | Measured ()
Delay (s) | 3.0 | 0.0625 | (0.06003, 0.00029)
Time of Delay (s) | N/A | 3.0 | (2.9055, 0.00025)
Buffer Size (Bytes) | 394375 | 8000 | (7722.59, 36.94)
 | Network Calculus | PNP2 | 
Delay (s) | 3.0 | 0.0625 | (0.06003, 0.00029)
Time of Delay (s) | N/A | 3.0 | (2.9055, 0.00025)
Buffer Size (Bytes) | 394375 | 8000 | (7722.59, 36.94)
NC

## Slide 14
PNP2

## Slide 15
PNP2

## Slide 16
NC

## Slide 17
NC

## Slide 18: Analysis of Periodic Systems (1/5) : Overview
Many systems exhibit some form of periodicity, where a system is periodic if the data production, service, or consumption (p/s/r) rate is a periodic function of time
  Time-integral of periodic data rates is the cumulative data (p/s/r) rate in the system. These cumulative functions are called repeating functions.
We wish to analyze the behavior of the system, specifically by looking at the system’s outputs
  If we show that the system’s outputs exhibit periodicity, we can show that the system has no unbounded buffer growth
We will examine two periodic systems and analyze how their behavior changes over the course of two periods.

## Slide 19: Analysis of Periodic Systems (2/5) : System 1
Notes: Put line indicating period

## Slide 20: Analysis of Periodic Systems (3/5): System 2

## Slide 21: Analysis of Periodic Systems (4/5): Formal Definitions
We define a function to be repeating :
  Where is periodic
  Repeating functions result from integrating periodic functions; they produce periodic functions when differentiated
Analyze a deterministic, repeating queuing system defined by:
  : data service capacity of the network
  : input data to the network
  : output data transmitted on the network
  : amount of data in the system’s buffer,
  : remaining service capacity of the network after servicing , i.e.
  : hyperperiod of the input function period and the service function period ,

## Slide 22: Analysis of Periodic Systems (5/5): Stability Analysis
Consider the scenario when ,
  is a measure of how much extra data the network can transmit in a given period; not all of the data in the buffer will have been serviced by the end of the second period, therefore
  For any two successive periods, and
    Therefore the system has unbounded buffer growth
Consider the scenario when ,
  The network can service in a period the amount of data remaining in the buffer from the preceding period, therefore
  For any two successive periods, and
    Therefore the system has a finite buffer
Notes:   mention tipping point and having a margin around it

## Slide 23: PNP2 Analysis of TDMA
Time Division Multiple Access (TDMA) is a Medium Access Control (MAC) protocol designed to minimize the number of packet collisions
  Allocates time slices to each transmitter during which only they are allowed to send
  The sequence of time slices repeats with a certain period
  MAC layer protocols can affect the performance of the application adversely and so must be taken into account when analyzing the system
By integrating such low-level protocol behavior models into the network model, we can more precisely predict the performance of the applications
Given:
  : the period of the TDMA schedule
  : the duration of node ’s TDMA slot
  : the bandwidth available to node during its slot
We calculate:
  : the perceived bandwidth available to the node during the TDMA period
  : the change in the predicted delay experienced by application traffic
  : the change in the predicted buffer space required for the application
Notes: Specifically mention way up front that it’s periodic/cyclic in TDMA ROUNDS

## Slide 24: PNP2 Analysis of TDMA
Since
  is dependent on
  is bounded by
  is governed by
Minimizing minimizes both the maximum extra delay and maximum extra buffer space
Notes: Without using a detailed model of TDMA we can get valid analysis results
Explain based on shared bandwidth

## Slide 25: PNP2 Compositional Analysis
Goal: allow applications to be analyzed separately, derive performance prediction for each application
Compositionality: when a system’s properties can be derived from the properties of its components and how they are interconnected
Composability: when components’ properties do not change when it is composed with other components
Must define the way applications’ profiles share their node’s resources and formalize mathematically the sharing of the resources

## Slide 26: PNP2 Compositional Analysis
To determine the way in which a node provides network capacity to its applications, we assign each application flow in the system a unique priority,
  Applications serviced in strict order according to priority
  Profile has a higher priority than profile
  A profile does not receive any service from a node until all other profiles with higher priority have been serviced by that node
    In this way, lower priority applications’ data may be buffered if the node has no remaining capacity at the time
Mathematically, a node’s remaining service profile after it provides service profile to an application profile is
  Where we define addition and subtraction of profiles,
Notes: Making the assumption/point works because we can add/subtract linearly
Mention TC/dscp

## Slide 27: PNP2 Delay Analysis
Given a profile describing delay in the network as a function of time, we can calculate its effect on a data profile:
  : the data’s profile which is being delayed, e.g. transiting a link
  : the delay profile describing latency as a function of time
  : the received profile describing the data vs. time as it is received after being delayed
Notes: Mention WHY? : want to analyze networks which have variable delays
Linear continuous delay function
Just mention talk here about the periodicity and the requirement that the delay profile be periodic

## Slide 28: PNP2 Analysis of Statically Routed Networks
Goal: support for analysis of routed networks
  Special case of routing in ad-hoc networks, where one or more nodes can route messages for other nodes
  Incorporate the compositional and delay analysis to support routed network analysis
Assumptions:
  Not considering transmission error or data corruption
  Cut-through routing / wormhole switching
    Routers forward all packets without integrity checking
    Lower latency than store and forward routing
  Static routing
    Routes packets will take are known at design-time
  Enforcement of profile priority in transmission and routing packet scheduling
Notes: Mention that this is mostly relevant to wired networks

## Slide 29: PNP2 Analysis of Statically Routed Networks
Iteratively analyze system configurations
  Analyze sender profiles in priority order
  Every time a required profile is convolved with a receiver profile or a provided profile, calculate the remaining capacity of the profile
Handles interfering, independent flows
  E.g. two routed flows passing through the same router along different paths
analyze( profiles )
profiles = sorted( profiles, priority )
for sender in profiles
transmitted_nodes = list.empty()
required = sender
for receiver in sender.receivers()
route = getRoute( required, receiver )
for node in route
provided = node.provided()
// CALCULATE
output = convolve( required, provided )
remaining = provided – output
received = delay( output, provided )
// UPDATE
node.provided( remaining )
required = received
transmitted_nodes.append( node )
final = convolve( required, receiver )
receiver = receiver – final
Notes: Mention that we can handle whether the system supports multicast or not

## Slide 30: PNP2 Analysis of Statically Routed Networks
Example system configuration for analysis validation

## Slide 31: PNP2 Analysis of Statically Routed Networks
Measure total delay from the time the sender transmits the data to the time the receiver receives the data
  Includes all buffer, processing, and transmission delays
Resultant delay measurements are conservative
  Not as tight because Linux TC does not perfectly constrain the flows to their allotted bandwidth; some bursts occur that greatly exceed the profile
  Shows that our profile composition, delay, and routing analysis techniques can be useful for deriving conservative bounds in systems with statically routed networks
 | Predicted | Measured ()
High Priority Flow Delay (s) | 8.96 | (4.1436, 0.00929)
Low Priority Flow Delay (s) | 15.7775 | (13.0460, 0.01344)
 | Predicted | 
High Priority Flow Delay (s) | 8.96 | (4.1436, 0.00929)
Low Priority Flow Delay (s) | 15.7775 | (13.0460, 0.01344)

## Slide 32: PNP2 Run-Time Measurement, Detection, Enforcement
Can our design-time modeling and analysis better inform our run-time implementation?
Integrate design-time models and semantics into run-time software component-based middleware
  Component is the smallest deployable part of an application containing:
    Timers: a timer provides a periodic event trigger to the component
    Input/Output ports; we’re specifically focusing on publish/subscribe
    A single thread which executes all events for the component in FIFO order without preemption
Notes: Mention application? Deployment?

## Slide 33: PNP2 Run-Time Measurement, Detection, Enforcement
Integrated measurement and enforcement code into the middleware on the sender side
  All application traffic must go through the middleware
  If the traffic does not conform to the application’s profile the middleware discards it and throws an error to the application
Sender and receiver code automatically record the measurements of traffic that is sent/received

## Slide 34: PNP2 Run-Time Measurement, Detection, Enforcement
Developed traffic production code which runs in the application and produces traffic according to the sender profile
Similar code in the receiver which pulls data from the receiver’s buffer according to the receiver’s profile

## Slide 35: PNP2 Distributed Denial of Service (DDoS) Detection
DDoS attacks are generally classified as excessive traffic from a large amount of (possibly heterogeneous) sources targeted towards a single point or a single group
The receiver has a finite receive buffer and a specified profile governing the rate at which it can pull data from the buffer
  Senders who send too much data may cause the buffer to fill up, causing data from well-behaved senders to be lost
  If we can detect which senders are misbehaving and prevent them from sending, well-behaved senders will not see any degradation of service
Developed an out-of-band (OOB) communications channel from the sender middleware to the receiver middleware
  Invisible to the application
  Allows the receiver to communicate with and control the sender’s middleware
Works because we know precisely the correct behavior of applications and we know all of the communication patterns and we have a trusted middleware

## Slide 36: PNP2 Distributed Denial of Service (DDoS) Detection
Algorithm on the receiver for determining which senders are sending too much data to the receiver
  Receiver knows the profiles of all of its senders
  When the buffer is emptied (or at some other condition) the senders can be re-enabled

## Slide 37: PNP2 Distributed Denial of Service (DDoS) Detection
Developed test application with multiple communications flows
Some of the senders are configured to misbehave
  Receiver’s buffer would overflow and the good senders’ data would be dropped
Using our OOB channel, we automatically detect the misbehaving senders, stop them from sending, and prevent the buffer from overflowing

## Slide 38: Conclusions and Future Work
Presented new modeling and analysis techniques for networked CPS based on (min,+)−𝑐𝑎𝑙𝑐𝑢𝑙𝑢𝑠
  Convolution
  Composition
  Delay
  Developed analysis for periodic / repeating systems
  Demonstrated analysis of low layer protocols and their effect on application traffic
Developed run-time network management based on design-time analysis
  Allows detection and mitigation of DDoS attacks
To make this work more applicable
  Model/Analyze other transmission protocols, e.g. TCP
  Model/Analyze other MAC protocols, e.g. CSMA
  Incorporating packet loss and transmission errors
  Researching data-dependent traffic modeling
  Timing and time synchronization analysis

## Slide 39: Publications
W. Emfinger and G. Karsai. Modeling network medium access protocols for network quality of service analysis. In Proceedings of the 18th IEEE Symposium on Real-Time Computing (ISORC), ISORC ’15, pages 44–47, Auckland, New Zealand, 2015. IEEE
W. Emfinger, G. Karsai, A. Dubey, and A. Gokhale. Analysis, verification, and management toolsuite for cyber-physical applications on time-varying networks. In Proceedings of the 4th ACM SIGBED International Workshop on Design, Modeling, and Evaluation of Cyber-Physical Systems, CyPhy ’14, pages 44–47, New York, NY, USA, 2014. ACM
W. Emfinger, P. Kumar, A. Dubey, W. Otte, A. Gokhale, G. Karsai. DREMS: A Toolchain for the Rapid Application Development, Integration, and Deployment of Managed Distributed Real-time Embedded Systems. In Proceedings of the IEEE Real-Time Systems Symposium, RTSS@Work 2013, Vancouver, Canada, 2013. IEEE
P. S. Kumar, W. Emfinger, A. Kulkarni, G. Karsai, D.Watkins, B. Gasser, C. Ridgewell, and A. Anilkumar. Rosmod: A toolsuite for modeling, generating, deploying, and managing distributed real-time component-based software using ros. In Rapid System Prototyping Symposium (ESWEEK), Amsterdam, The Netherlands, 2015

## Slide 40: Publications
P. S. Kumar, W. Emfinger, and G. Karsai. A testbed to simulate and analyze resilient cyber-physical systems. In Rapid System Prototyping Symposium (ESWEEK), 2015
Pradhan S., W. Emfinger, A. Dubey, W. Otte, A. Coglio, D. Balasubramanian, A.Gokhale, G. Karsai. Establishing secure interactions across distributed applications in satellite clusters. In Proceedings of the IEEE International Conference on Space Mission Challenges for Information Technology, SMC-IT, 2014, Laurel, MD, USA. IEEE
Balasubramanian, D., W. Emfinger, P. S. Kumar, W. Otte, A. Dubey, and G. Karsai. An application development and deployment platform for satellite clusters. In Proceedings of the Workshop on Spacecraft Flight Software, 2013
Balasubramanian, D., A. Dubey, W. R. Otte, W. Emfinger, P. Kumar, and G. Karsai. A Rapid Testing Framework for a Mobile Cloud Infrastructure. In Proceedings of the IEEE International Symposium on Rapid System Prototyping, RSP, 2014. IEEE

## Slide 41: Publications
Dubey, A., W. Emfinger, A. Gokhale, G. Karsai, W. R. Otte, J. Parsons, C. Szabo, A. Coglio, E. Smith, and P. Bose. A Software Platform for Fractionated Spacecraft. In Proceedings of the 2012 IEEE Aerospace Conference, Big Sky, Montana, 03/2012. IEEE
Levendovszky, T., A. Dubey, W. R. Otte, D. Balasubramanian, A. Coglio, S. Nyako, W. Emfinger, P. Kumar, A. Gokhale, and G. Karsai. DREMS: A Model-Driven Distributed Secure Information Architecture Platform for Managed Embedded Systems. In IEEE Software, vol. 99: IEEE Computer Society, 2014. IEEE
Submitted, Awaiting Review:
  W. Emfinger, P. Kumar, A. Dubey, G. Karsai. Towards Assurances in Self-Adaptive, Dynamic, Distributed Real-time Embedded Systems. In Software Engineering for Self-Adaptive Systems: Assurances, 2015.

## Slide 42: References
L. Thiele, S. Chakraborty, and M. Naedele. Real-time calculus for scheduling hard real-time systems. In in ISCAS, pages 101–104, 2000.
A. Varga and R. Hornig. An overview of the omnet++ simulation environment. In Simutools ’08: Proceedings of the 1st international conference on Simulation tools and techniques for communications, networks and systems & workshops, pages 1–10, ICST, Brussels, Belgium, Belgium, 2008. ICST (Institute for Computer Sciences,Social-Informatics and Telecommunications Engineering).
L. Rizzo. Dummynet : a simple approach to the evaluation of network protocols. ACM SIGCOMM Computer Communication Review, 27(1):31–41, 1997.
D. Mahrenholz and S. Ivanov. Real-time network emulation with ns-2. Proceedings- Eighth IEEE International Symposium on Distributed Simulation and Real-Time Applications, DS-RT 2004, pages 29–36, 2004.
J.-Y. Le Boudec and P. Thiran. Network Calculus: A Theory of Deterministic Queuing Systems for the Internet. Springer-Verlag, Berlin, Heidelberg, 2001.

## Slide 43: References
D. G. Kendall. Stochastic Processes Occurring in the Theory of Queues and their Analysis by the Method of the Imbedded Markov Chain. The Annals of Mathematical Statistics, 24(3):338–354, 1953.
Gilberto Flores Lucio, Marcos Paredes-farrera, Emmanuel Jammeh, Martin Fleury, and M. J. Reed. OPNET Modeler and Ns-2: Comparing the Accuracy of Network Simulators for Packet-Level Analysis using a Network Testbed. 3rd WEAS International Conference on Simulation, Modelling and Optimization (ICOSMO), pages 700–707, 2003.
G. Giambene. Queuing Theory and Telecommunications Networks and Applications. 2005.
R. L. Cruz. A calculus for network delay–I: Network elements in isolation. IEEE Transactions on Information Theory, 37(1):114–131, 1991.
O. S. Consortium et al. Openflow switch specification version 1.0. 0, 2009.
M. Carbone and L. Rizzo. Dummynet revisited, 2010

## Slide 44: Questions?
Thank you for your attention!

## Slide 45: PNP2 Delay Analysis
How does the delay affect the periodicity of the profile?
  What is the scenario in which the period of is the same as the hyperperiod of and ?
  The period of is the difference between its start time and end time
Given:
  : the hyperperiod of the link profile and the delay profile
  : the beginning of the received profile,
  : is the end of the received profile,
We can find the condition for which the periodicity of the profile is unchanged:
  Which confirms that the periodicity of the delayed profile is unchanged from the link profile the latency profile is periodic, i.e.

## Slide 46: PNP2 Analysis of Statically Routed Networks
System configuration
  : set of all profiles
  : set of all nodes
  : set of all routes in the system
Profile
  : the node ID on which the profile exists
  : the kind of the profile,
  : the period of the profile
  : the flow ID of the profile; belong to the same flow
  : the priority of the profile; has a higher priority than
  : set of tuples describing how each variable varies with respect to time.
Node
  : ID of the node
  : the node’s provided profile
Route
  Where
Notes: Keep as backup slide

## Slide 47: PNP2 Analysis of Statically Routed Networks
Configuration of priority enforcement on the routing node

## Slide 48: PNP2 Network Applications Testbed
Used for the deployment of PNP2 tests
Have experimentally validated PNP2 analysis results using our testbed
Will be useful in developing and testing new research in networked cyber-physical systems

## Slide 49: Generation of Application Network Profiles from Business Logic Models (2/3)
Notes: 2 component-based applications (shades of blue) split across 4 nodes in a cluster
Apps communicate with each other
All port traffic flows on the network

## Slide 50: Generation of Application Network Profiles from Business Logic Models (1/3)
Component-based Software Engineering Overview
A component is the smallest deployable part of an application, containing
  Timers & State Variables
  External interfaces (input and output ports), their associated input callbacks or output handles
  A single thread which sequentially processes to completion pending component operations
Components can be only triggered by
  Timer expiry
  Callback invocation for data arriving on an input port
An application consists of a group of single-threaded components which cooperate together and are deployed as a unit
Applications are complex and difficult to analyze
  By using component-based software design and developing models based on the components, we can make analysis tractable
Notes: Don’t get into depth about CPN or anything

## Slide 51: Network Application Fault/Anomaly Classification
We will use our testbed to run distributed network tests to classify certain types of anomalies, e.g. DDoS attacks from compromised applications within the cluster.
  Cluster is a managed system; we have full control over all layers on each node, but not the applications
We will use the network resource utilization measurements gained from the tests to derive metrics which allow us to differentiate between classes of behavior, e.g. standard/stable application behavior vs. DDoS behavior.
We will then use the classifications to show that the system can detect these types of attacks, mitigate their propagation, and report the attack to the system's manager.
Notes: Since/if we know expected behavior, we can detect deviations from expected behavior;
This is a managed system, we have full control over the layers in every node, but not over the applications